UNBUNDLED

LOOPS

INSTALLATION, TESTING

AND MAINTENANCE

GUIDELINES

Version 2

BPWG Approval: March 18, 2002

CRTC Approval:

Revision History

| Date | Version | Comments |
| --- | --- | --- |
| October 18, 1998 | 1 | Version 1 issued |
| February 15, 2002 | 2 | This Version 2 reflects proposed changes to approved Version 1 of the guidelines as discussed over time by the Working Group. Changes from official Version 1 are highlighted. The Working Group has achieved consensus on Section 7.3 Connecting Link Repair Process and this process was implemented February 3, 2002. |
| March 18, 2002 | 2 | Further modifications made and consensus reached by BPWG. Document to be forward to CISC for approval. Implementation will take effect within 60 days of CISC approval. |

TABLE OF CONTENTS	Page #

1.	OVERVIEW	5

1.1	DEFINITIONS	5

2.	OBJECTIVE	6

3.	GENERAL RESPONSIBILITIES	6

3.1	COMPETITIVE LOCAL EXCHANGE CARRIER (CLEC)	6

3.2	INCUMBENT LOCAL EXCHANGE CARRIER (ILEC)	8

4.	INSTALLATION AND TESTING	9

4.1	INSTALLATION	9

4.1.1	GENERAL	9

4.1.1.1	Loop Type A	10

4.1.1.2	Loop Type B	11

4.1.1.3	Loop Type C	12

4.1.2	CONNECTING LINKS	13

4.1.3	JEOPARDY NOTIFICATION	14

4.1.4	UNBUNDLED LOOP PROVISIONING FAILURES	14

4.1.5	SERVICE ORDER ACTIVITY	14

4.1.6	DEMARCATION	15

4.1.7	CUSTOMER TRANSFERS BETWEEN LECs AND MANAGEMENT OF ILEC LOOP FACILITIES.	15

4.1.7.1	Customer Transfers Between LECs	15

4.1.7.2	Management of ILEC Loop Facilities	15

4.1.8	COMPLETION NOTIFICATION ON NEW AND MIGRATING LOOPS	16

4.1.8.1	 Migrating Loops	16

4.1.8.1.1 	Requirements	16

4.1.8.1.2 	Solution	16

4.1.8.1.3	Process	16

4.1.8.2    Field Visit Orders for New loops or Migrations	16

4.2	TESTING	18

4.2.1	LOOP TYPES	18

4.2.1.1	Loop Type A	18

4.2.1.2	Loop Type B	18

4.2.1.3	Loop Type C	18

4.2.2	ADDITIONAL TESTING	18

4.2.3	TEST SETS	18

5.	ESTABLISHING INTERFACES	19

6.	MAINTENANCE	20

6.1	GENERAL	20

6.1.1	INOPERATIVE AND IMPAIRED CONDITIONS	20

6.1.2	SECTIONALIZATION PROCESS	20

6.1.3	“CALL BEFORE YOU DIG”	21

7.	TROUBLE REPAIR	22

7.1	RESPONSIBILITIES	22

7.2	UNBUNDLED LOOP REPAIR INTERVALS	22

7.3	CONNECTING LINK REPAIR PROCESS	22

7.4 	REPAIR VERIFICATION TESTS	25

8.	TROUBLE REPORTING	25

8.1	GENERAL	25

8.2	TROUBLE REPORT INFORMATION	26

8.3	TROUBLE CLEARANCE REPORTING	26

9.	EXCEPTIONS	26

9.1	REQUEST FOR COOPERATIVE TESTING	26

10.	ADDITIONAL BILLING	27

11.	ESCALATION	27

12.	APPENDICES:	28

APPENDIX 12.1: 	Escalation contacts	28

APPENDIX 12.2 : 	 Escalation intervals	28

APPENDIX 12.3:	SERVICE ASSURANCE PROCESS:	29

APPENDIX 12.4: ACRONYMS:	32

# 1.	OVERVIEW

On August 1, 1996, the CRTC issued Telecom Public Notice 96-28 on the Implementation of Regulatory Framework - Development of Carrier Interfaces and Other Procedures establishing the CRTC Interconnection Steering Committee (CISC) process to oversee the process of identifying the requirements and developing the administrative and support systems required to facilitate local telephone competition.  Subsequently on May 1, 1997 Telecom Decision CRTC 97-8 reaffirmed its support for the CISC and its working groups.

This document has been developed by the Network Operations Working Group (BPWG) to provide the operations personnel of the respective Local Exchange Carriers (LECs) with general guidelines for installation, testing and maintenance of unbundled loops.

This document does not replace or supercede any Tariffs, Contracts or other legally binding documents.  In the case of conflict between this document and any legally binding document, the latter document will prevail.

## 1.1	DEFINITIONS

Local Exchange Carrier (LEC): 	as referred to in this document, is an exchange carrier that has been approved by the CRTC to provide local exchange services.

Incumbent Local Exchange Carrier (ILEC): 	as referred to in this document, is the LEC providing unbundled loops to a Competitive Local Exchange Carrier (CLEC).

Competitive Local Exchange Carrier (CLEC): as referred to in this document, is defined as the LEC that is leasing unbundled loops from a ILEC.

End User: 	is the customer of a Local Exchange Carrier.

A CLEC may request the ILEC to provide various unbundled facilities to be used as part of the CLEC’s network arrangement as per CRTC decision 97-8.

The ILEC may provide unbundled local loops, where available, as set in its applicable tariffs.

Specific operational procedures may be required between the ILEC and the CLEC.

# 2.	OBJECTIVE

The objective of this document is to provide efficient guidelines for the installation, testing and maintenance of unbundled loops.

This objective can only be attained through a positive working relationship between the CLEC and the ILEC, and through mutual acceptance of appropriate responsibilities.

The purpose of these guidelines is to provide details related to the CLEC and ILEC interface processes for the installation, testing and maintenance of these services.

# 3.	GENERAL RESPONSIBILITIES

This section describes the individual responsibilities for the various groups involved in the installation, testing and maintenance of unbundled local loops.

## 3.1	COMPETITIVE LOCAL EXCHANGE CARRIER (CLEC)

The CLEC has the following responsibilities:

- Provide and maintain appropriate levels of adequately trained personnel.

- Act as its End User customer contact in all matters involving installation, testing and maintenance of CLEC provided services.

- Coordinate with the ILEC to ensure that unbundled loops are installed in working order on the committed due date and to the specifications as requested in accordance with the Local Service Request (LSR).

- Where analogue dial-tone service is being provisioned, the CLEC will ensure that dial tone is present on the loop connecting link associated with a leased loop order no later than 8:00 A.M., local time in provisioning LEC territory, on the Due Date

- Coordinate with the End User and the ILEC, to minimize service interruption to the End User.

- When a CLEC migrates a loop associated with Customer Premise Equipment (CPE), the CLEC is responsible to advise the End User to contact their CPE provider.

- Notify the ILEC of any changes affecting the service requested, including the service due date.

- Maintain adequate circuit records.

- Provide a contact number for accepting trouble reports that is readily accessible 24 hours a day, 7 days a week.

- Accept trouble reports from their End Users.

- Dispatch its own maintenance forces.

- Ensure that test equipment is capable of measuring the parameters set forth in the Loop Technical Specifications.

- Ensure that the test equipment used is adequate to properly test the services offered to the end user.

- Sectionalize and analyze it’s own network prior to referring any trouble to the ILEC.

- Keep its End User advised of the status of trouble reports, as appropriate.

- Test cooperatively, when necessary, with the ILEC to further identify and clear an existing trouble when the trouble has been sectionalized to the ILEC provided unbundled loop.

- Where required, the CLEC is responsible for disconnecting the terminal equipment from the unbundled loop to facilitate testing by the ILEC.

- When placing a request for an unbundled loop(s), the CLEC will provide the appropriate information on the Local Service Request (LSR) in accordance with the Canadian Local Ordering Guidelines (C-LOG).

- Provide the ILEC with access to locations under the CLEC’s control.

## 3.2	INCUMBENT LOCAL EXCHANGE CARRIER (ILEC)

The ILEC has the following responsibilities:

- Provide and maintain appropriate levels of adequately trained personnel.

- Provide unbundled loops, where available, to the CLEC according to the applicable ILEC tariffs.

- Cooperate with the CLEC to ensure that the loops are installed in working order on the committed due date and to the specifications as requested in accordance with the LSR.

- Cooperate with the CLEC to ensure minimum service interruption to the End User.

- Notify the CLEC of any changes affecting the service requested, including the service due date.

- Notify the CLEC of any facility shortages as soon as known.

- Maintain complete and accurate installation and repair records.

- Provide a contact number for accepting trouble reports that is readily accessible 24 hours a day, 7 days a week.

- Dispatch it’s own maintenance forces.

- Sectionalize- and clear- the trouble in it’s own network.

- Keep the CLEC advised, when necessary, of the trouble status.

- Test cooperatively, when necessary, with the CLEC to further identify and clear an existing trouble when the trouble has been sectionalized to the CLEC network.

# 4.	INSTALLATION AND TESTING

The following outlines the guidelines to be followed for installation and testing activities associated with ILEC provided unbundled loops.

## 4.1	INSTALLATION

### 4.1.1	GENERAL

Installation, as used in this document, refers to that portion of the provisioning process which starts when a request for an unbundled loop(s) service is received by the operations group of the ILEC and ends when the loop is made available, in working order and provisioned per the specifications requested on the LSR by the CLEC, on the Due Date. The request could be for new installations, migrations, and changes or disconnects.

Technical specifications have been developed for the ILEC loop types and categories with specific characteristics and objective limits.  Current technical specifications should be available to the ILEC and CLEC technicians to define the loop parameters for installation and testing.  The following loop types are currently available:

### 4.1.1.1	Loop Type A

Unbundled Type A Loops Categories 1, 2, 3, and 4, provide an analogue transmission facility which extends from the Central Office Loop Termination (COLT) or Point of Termination (POT) to the Customer Network Interface (CUST-NI) and which is intended to facilitate the transmission of voice grade signals of approximately 3 kHz usable bandwidth.  The electrical interface at the POT and the CUST-NI shall be a 2-wire metallic interface.  This transmission path may be derived over any number of different types of technologies, but not limited to: metallic paired cable; metallic paired cable with loading coils and /or build out capacitors; metallic pair based analogue or digital loop carrier systems; and optical fibre based digital loop carrier systems.  If metallic paired cable is used to provide the access, there may be bridged tap present.  Additionally, in some cases different facility technologies may be used in tandem.

Unbundled Type A Category 5 Loops provide a transmission facility which extends from the POT to the CUST-NI and is intended to facilitate the transmission of signals above voice band, viz. the voiceband is considered to be approximately 300 to 3400 Hz.  The electrical interface at the POT and the CUST-NI shall be a 2-wire metallic interface. The Unbundled Type A Category 5 Loop will be provided over metallic unloaded facilities.

### 4.1.1.2	Loop Type B

Unbundled Type B Category 1 Loops provide transmission facilities which extend from the COLT or POT to the CUST-NI and are intended to facilitate the transmission of ISDN BRA signals, viz. a maximum of 2 B + 1 D channels.  The electrical interface at the COLT or POT and the CUST-NI shall be a 2-wire metallic interface.

The transmission path may be derived over any number of different types of technologies, but not limited to: metallic paired cable; or a carrier system designed to support an ISDN BRA signal.  Additionally, in some cases different facility technologies may be used in tandem.

The Unbundled Type B Category 2 Loop will be provided over metallic unloaded facilities.

### 4.1.1.3	Loop Type C

A Type C Unbundled Local Loop is a digital transmission path which extends from the CUST-NI to the COLT and supports the transmission of an ISDN PRI (Primary Rate Interface) type signal terminating in a 4-wire electrical interface at both the end-customer’s premises and the Company’s CO building.

### 4.1.2	CONNECTING LINKS

A transmission path which connects a Company-provided unbundled network component located or terminated within the Company’s CO building to the CLEC’s co-located transmission equipment located within the Company’s CO building.

The initial request and subsequent addition of connecting links are ordered through the co-location process.  Loop connecting links are at a DS 0 rate and are used for both Loop Types A and B.

Connecting Links for Type C Loops are at a DS 1 rate.

### 4.1.3	JEOPARDY NOTIFICATION

Any situation, which threatens the completion of the service order on the Due Date, shall be shared between the LECs as soon as such situations are identified to minimize End User service disruption.

### 4.1.4	UNBUNDLED LOOP PROVISIONING FAILURES

Where, on the Due Date, a trouble is encountered on the migration of an unbundled loop, or on the installation of a new unbundled loop, the LECs will, on a best effort basis, take all necessary steps to ensure that the unbundled loop and/or connecting link trouble is cleared on that same day.

The order for the unbundled loop service is considered complete by the loop provider when the loop is provisioned in working order and as specified on the LSR.

### 4.1.5	SERVICE ORDER ACTIVITY

It is understood that the CLEC would have ordered the required service from the ILEC CSG or equivalent organization.  Where a standard service order interval has not been established, the CSG or equivalent will negotiate service intervals on an individual case basis. Throughout the installation period, all CLEC inquiries will be referenced by the ILEC Exchange Carrier Circuit ID (ECCKT) and/or LSR Purchase Order Number (PON).

The CLEC is responsible to coordinate with the End User and to provide the appropriate information to the ILEC to ensure that the unbundled loop is installed in accordance with its End User requirements.

When a new unbundled loop is installed in working order and to the specifications requested on the LSR (LSR to be modified to include a field that indicates if dial tone is to be present on the loop), the ILEC will call the CLEC on either the local or toll free number to provide completion notification.

When a CLEC migrates a loop with CPE, the CLEC is responsible to advise the End User to contact their CPE provider.

Each LEC is responsible for the service or portion of service that it is providing. CLECs and ILECs must ensure the respective segments have been ordered, designed and installed correctly before completing their respective internal service orders.

When necessary, the ILEC will dispatch a field technician to the CLEC’s End User site to install the requested loop facility(s) up to the demarcation point or CUST-NI.

### 4.1.6	DEMARCATION

The Commission has provided definitions of demarcation point in Telecom Decision CRTC 99-10 entitled Location of Demarcation Point for Inside Wire in Multi-Dwelling Units and Associated Issues. Demarcation guidelines and definitions will be respected in accordance with this Decision, approved CISC consensus and any future CRTC directives.

### 4.1.7	CUSTOMER TRANSFERS BETWEEN LECs AND MANAGEMENT OF ILEC LOOP FACILITIES.

### 4.1.7.1	Customer Transfers Between LECs

a.	Where the LEC currently serving an end-customer (“Current LEC”) is using an ILEC loop, and the LEC acquiring this end-customer (“New LEC”) requests the transfer of the ILEC loop to provide local service to this end-customer, the ILEC will go to the same efforts to provision the loop to the demarcation point without requiring the New LEC to visit the end-customer premises, as if that ILEC were, itself, acquiring the end-customer.

b.	Where an ILEC loop is not used by the Current LEC, or where there is no local telephone service currently provided to the service address, and the New LEC requests an ILEC loop to provide service to an end-customer, an end-customer premise visit may likely be required by the New LEC to ensure the connection between the end-customer’s inside wire and the ILEC loop.

### 4.1.7.2	Management of ILEC Loop Facilities

Where an ILEC requires changes to the physical components of a local loop, either in the initial migration of the loop or during its ongoing use, the ILEC will manage the loop facilities to maintain the terminating end of the loop at the existing demarcation point and not require a CLEC end-customer premise visit, as if that ILEC were, itself, serving the end-customer.

However, where the ILEC must physically relocate the terminating end of an ILEC loop at the demarcation point (e.g. due to maintenance), an end-customer premise visit may be required by the CLEC, and, in such case, the ILEC will co-ordinate relocation of the loop termination with the CLEC to maintain the connection and minimize the service interruption between the end-customer’s inside wire and the ILEC loop.

### 4.1.8	COMPLETION NOTIFICATION ON NEW AND MIGRATING LOOPS

### 4.1.8.1	 Migrating Loops

During the customer transfer process, a specific series of activities must take place in a particular order to ensure that End Users do not face extended service outages during migration from one local service provider to another.  In particular, the process clearly indicates that a facility provider (the ILEC) must notify the ordering carrier (the CLEC) once the physical work is completed in a loop “migration” scenario with Local Number Portability (LNP) to ensure that the migrating customers’ ability to receive incoming calls will be restored on a timely basis.  In the provisioning of a Type A loop migration from one carrier to another, the facility provider (the ILEC) must perform specific activities at the time of the CO cutover.

### 4.1.8.1.1 	Requirements

The notification process is based on the following assumptions/requirements:

- Where analogue dial-tone service is being provisioned CLEC’s will ensure that dial tone is present on their side of the loop connecting link associated with a leased loop order no later than 8:00 A.M., local time in provisioning LEC territory, on the Due Date

- A frame cutover of the CO jumper is required to complete this order.

- The CLEC network will provide a call completion/termination signal to the 555-0974 caller within 3 ring cycles.

### 4.1.8.1.2 	Solution

Telephone number 555-0974 has been reserved for this purpose across Canada.  LEC’s will establish the necessary hardware and software, and arrange for pre-service testing with the ILEC, through the BPWG for completion notification.  At the completion of the testing, the ILEC will consider the solution to be “in service” and will ensure that completion of subsequent orders, which qualify, will include the 555-0974 notification. If there is no dial tone present or the loop is not analogue a toll free/local number will be provided by the CLEC for ILEC notification.

### 4.1.8.1.3	Process

Upon completion of the physical frame work, the technician will connect to the leased loop, place a call to the 555-0974 telephone number, wait for an indication of call completion, then disconnect from the loop or dial the toll free/local number to notify the CLEC that the ILEC work has been completed.

### 4.1.8.2  Field Visit Orders for New loops or Migrations

In addition, where an installer visit is required to complete the order the installer will place a phone call to a local or toll free number, provided by the CLEC on the service order, to inform the CLEC of the completion of the field work, including testing to the demarcation point. The completion notification will include:

- Circuit ID

- Exact Physical location of demarcation.

(N.B. If the demarcation point on migration changes then this information is required. If the demarcation point does not change this information is not required)

Some demarcation locations are:

- Main Terminal Room (MTR)

- Riser/Wire Closet

- Customer Suite/Unit

Example of information provided: Location - MTR, Floor - 12 and Tower  - 3

4.1.8.3	 Scenarios

|  | SCENARIO | FIELD VISIT | NOTIFICATION REQUIRED | BY WHOM | SOLUTION |
| --- | --- | --- | --- | --- | --- |
| 1. | LNP - Reuse of existing loop facility | N | Y | C.O. | Call to 555-0974 or (See Note 1) |
| 2. | LNP - With new loop new facility | Y | Y | FIELD | Call to CLEC |
| 3. | LNP - New loop with reuse of existing facility | N | Y | C.O. | Call to 555-0974 or (See Note 1) |
| 4. | LNP only (No loop) | N | N | ---- | ----- |
| 5. | No LNP - Reuse of existing loop facility | N | Y | C.O | Call to 555-0974 or (See Note 1) |
| 6. | No LNP - With new loop, new facility | Y | Y | FIELD | Call to CLEC 1 |
| 7. | No LNP - New loop with reuse of existing facility | N | Y | C.O. | Call to 555-0974 or (See Note 1) |

Note 1:

When the ILEC is unable to complete the 555-0974 notification due to either no dial tone on the analogue loop or digital services have been ordered the ILEC will call either a toll free or local number provided by the CLEC.

## 4.2	TESTING

Testing requirements of a specific unbundled loop is dependent on the type of loop requested.  Specific loop parameters are covered in the appropriate Technical Specifications documents and should be available to technicians who are involved in the testing of unbundled loops.

### 4.2.1	LOOP TYPES

#### 4.2.1.1	Loop Type A

Loop Type A are existing plant facilities that the ILEC has in place today and are being used to provide services to their own End Users.  Testing is undertaken and completed at the original time of building the facility (cable installation).  In today’s environment these loops are not pre-tested again on an individual loop request.  In this respect, loops provided by the ILEC will not be pre-tested.

#### 4.2.1.2	Loop Type B

The facility used to provide a Loop Type B will be pre-tested before being turned over to the CLEC.  Specific testing requirements and acceptance limits are outlined in the Technical Specifications for Loop Type B.  Pre-testing may take place at the time of turnover to the CLEC or may be done in advance by the ILEC.  An existing loop that is currently providing a Loop B service will not be pre-tested when it is migrated to a CLEC.

#### 4.2.1.3	Loop Type C

Pre-Testing of the facility used for a Loop Type C will be pre-tested before being turned over to the CLEC.  Specific testing requirements and acceptance limits are outlined in the Technical Specifications for Loop Type C.

### 4.2.2	ADDITIONAL TESTING

In the case where additional testing is requested by either party (CLEC or ILEC) and the loop is found to be within the technical specification for that particular loop type, the LEC requesting the tests may be subject to additional billing.

### 4.2.3	TEST SETS

Test sets are required during the initial installation of loops and also during maintenance and trouble isolation.  Test sets used by the LECs must be capable of testing the services that are being provided to their End User and adequate to measure the parameters that are set forth in the Technical Specifications.  It is recommended that the test sets used to cooperatively test an unbundled loop be compatible.

# 5.	ESTABLISHING INTERFACES

The point of connection between the ILEC and CLEC facilities or equipment in the ILEC’s CO, is referred to as the Point of Termination (POT).  The POT provides an interface for testing and maintenance of the facilities and is the division of operational responsibility.  Typically the POT is a cross-connection block on the MDF, or in some cases the IDF, which is the ILEC termination of the Connecting Link cable from the co-location room.

The point of connection between the ILEC and CLEC’s facilities or equipment at the End Users premises, is the Customer Network Interface (CUST-NI) or demarcation point.  The CUST-NI provides an interface for the testing and maintenance of the facilities and is the division of operational responsibility.

The electrical interface for Loop Types A and B at both the POT and CUST-NI will be a 2-wire copper interface.  For Loop Type C, the electrical interface at the POT and CUST-NI will be a 4-wire copper interface.

# 6.	MAINTENANCE

## 6.1	GENERAL

Maintenance of unbundled loops is based on the premise that the ILEC and the CLEC have the responsibility for the performance of the service or portion of service under its control.  However, the ILEC or the CLEC detecting an unbundled loop trouble or service trouble, will take corrective action, as outlined below.  This does not include any responsibility for sectionalization beyond the POT or the repair of equipment or facilities owned by the other company.

Investigation of chronic troubles with unbundled loops will involve the exchange of information between the ILEC and the CLEC.   This activity may involve cooperative testing and may be handled as an impaired local loop trouble report.

Maintenance, or trouble repair, as used in this document, refers to that portion of the repair process which starts after a loop has been installed as ordered, and post-installation, a performance issue (trouble) has been detected in the unbundled loop facility by either LEC. It ends when the loop has been restored to the required specifications in working order and repair completion notification is received by the CLEC.

### 6.1.1	INOPERATIVE AND IMPAIRED CONDITIONS

There are two general classes of troubles; 1) Out of Service (OOS), which is a condition in which the unbundled loop does not work and 2)  an impaired unbundled loop which is a loop that exhibits intermittent failures or degraded transmission performance.

### 6.1.2	SECTIONALIZATION PROCESS

Upon receipt of a trouble report from an End User the CLEC will initiate specific scripting with the customer to try and determine if the problem is from the demarcation point towards the ILEC unbundled loop. The CLEC will complete remote testing to the best of its ability as per industry standard and prove the trouble beyond its area of responsibility and towards the ILEC unbundled loop. Then it will refer the trouble to the ILEC who will test, analyze and prove its facility. If the trouble proves to be in the unbundled ILEC loop, the ILEC will repair and notify the CLEC upon completion. In situations where the trouble is proven beyond the unbundled ILEC loop, the ILEC will refer the problem back to the CLEC for resolution.

Initial sectionalization of a trouble is the responsibility of the CLEC.  It is anticipated that additional sectionalization may involve cooperative testing. Both entities are expected to participate in this activity when required.

The ILEC will coordinate the isolation of the trouble within the ILEC loop facility.

### 6.1.3	“CALL BEFORE YOU DIG”

The Locate Center, or equivalent organization, is expected to provide the same level of service to all users in a competitive environment.  Users who have switched their local service provider will continue to have access to the Locate Center as they do today.  When an End User calls the CLEC, the CLEC will advise them to call the Locate Center directly.

# TROUBLE REPAIR

## 7.1	RESPONSIBILITIES

If the sectionalized trouble is at the CLEC side of the demarcation point, the CLEC will:

- Repair the trouble;

- Perform appropriate testing to determine if the trouble is cleared.

If the trouble is sectionalized to the facility side of the demarcation point, the trouble will be referred to the ILEC, who will perform the same activities listed above.

CLEC technicians will limit their repair activities to CLEC-provided facilities and/or equipment.  No attempt will be made to adjust or repair facilities or equipment belonging to the ILEC.

The CLEC may not rearrange, move, disconnect, remove or attempt to repair any equipment or facilities provided by the ILEC.

## 7.2	UNBUNDLED LOOP REPAIR INTERVALS

The ILECs will endeavor to provide the CLEC’s unbundled loop trouble reports with a repair service level comparable to what the ILEC’s provide their retail end customers.  This will be accomplished by utilizing the existing ILEC dispatch processes and procedures.  Extenuating repair circumstances, when identified by the CLEC will be prioritized as per the ILEC’s existing practices.  Example, unbundled loops used by doctors and emergency service personnel or businesses with a service outage.

## CONNECTING LINK REPAIR PROCESS

When the ILEC sectionalizes a trouble with a unbundled loop and proves it towards the connecting link and CLEC equipment, the following practice and [process map] is to be followed to restore service to the facility.  For purposes of this section the term CLEC is used to describe any customer of the ILEC's unbundled loops.

The underlying principle of the process is to restore service as soon as possible.

In the case of:

Virtual Colocation - the ILEC TRC is able to prove the integrity of the connecting link. The ILEC C.O. technician has access to both terminating ends of the Link and the ILEC can therefore, determine whether the link is defective or the trouble proves into the CLEC equipment.  If a connecting link change is requested by the CLEC, it will be executed as per the process described below.

Physical Colocation - the ILEC TRC can not test from both terminating ends of the link, and, therefore the ILEC cannot determine the integrity of the link without the assistance of the CLEC Technician.

In both virtual and physical co-location, the ILEC C.O. technician will remain on site while the ILEC TRC contacts the CLEC to identify the reported trouble.  If the CLEC is unable to participate in a cooperative test immediately and wishes to implement a change to the connecting link pair, the CLEC is required to provide a new assignment to the TRC within 3 minutes.  If a new assignment cannot be provided within this time frame the CLEC and/or ILEC may opt to terminate the call and the CLEC will contact the TRC when a new connecting link pair is available.  Both parties will execute the connecting link change coincident with notification of the new assignment.

In the event that the ILEC Central Office is not normally manned and the CLEC cannot provide the connecting link pair assignment during the initial TRC call referenced in the paragraph above, the ILEC will ensure that the C.O. technician will remain on site for a minimum of 15 minutes (or greater at the ILEC's discretion) thereafter to allow the CLEC a reasonable time in which to provide the new connecting link pair assignment and contact the TRC to perform the pair change.  If the CLEC cannot manage a new assignment in that timeframe, it is recognized that the ILEC C.O. technician may not be present thereafter and a new appointment will need to be arranged.

If the CLEC determines that a connecting link pair change is required to restore service, the ILEC C.O. technician will implement a connecting link pair change immediately.  If service is restored as a result of changing the connecting link assignment, it will be assumed that the trouble was either with the connecting link or with the CLEC's equipment.  If the service is not restored, a CLEC technician may have to be dispatched.

In physical co-locations, applicable tariff charges associated with the connecting link pair change can be determined only by a cooperative test.  Charges for connecting link repair processes should be applied in the following circumstances:

- to a CLEC if a cooperative test is performed and a trouble is determined to be in the CLEC network; or

- to an ILEC if a cooperative test is performed and a trouble is determined to be in the ILEC network or the connecting link.

When either LEC requests a cooperative test to be performed, both LECs agree to have a technician on site at a pre-determined time. If either LEC technician is not present at the pre-scheduled time and reasonable notice was not provided, applicable tariff charges pursuant to the missed appointment can be applied to the LEC not present.

In the event that a connecting link is determined to be defective subsequent to a cooperative test, the ILEC will not be required to repair the connecting link at that time. When an unacceptable level of defects has been reached (as determined by the CLEC), the CLEC may request the repair of the defective connecting links.    Where cooperative testing is required, allocation of charges will be determined by the results of the test and will also consider previous cooperative test determinations.

## 7.4 	REPAIR VERIFICATION TESTS

When a trouble has been closed out by the ILEC, the CLEC may perform a repair verification test.  If the CLEC repair verification test identifies a trouble condition(s), then cooperative repair verification tests may be requested.

# 8.	TROUBLE REPORTING

## 8.1	GENERAL

LECs are responsible for the acceptance of all trouble calls from their End User.  In situations where a LEC receives a trouble call from an end user they do not serve, the End User will be directed to contact their local service provider.

The CLEC should first perform tests to determine if a trouble is in its facility / equipment or service.  If the trouble is found in it’s facility / equipment or service, the CLEC will clear the trouble and no referral to the ILEC is necessary.  If the trouble is sectionalized by the CLEC to the ILEC loop facility, the trouble will be referred to the ILEC.  The ILEC will clear the trouble or, where necessary, will work cooperatively with the CLEC to sectionalize the trouble.

Information about the trouble report, which may be specific to the End User will be exchanged, as appropriate, to facilitate testing and trouble resolution.

To assist installation and repair forces to properly identify an End Users telephone number, access numbers for an automated number identification circuit, where available, may be exchanged on a bilateral basis.

An automated number identification circuit is a switch provided feature that will identify the End User telephone number.  It is recommended that this feature be provided by all LECs.

Investigation of chronic unbundled loop failures will involve exchange of information relative to the chronic failure.  Detailed investigation should be made to determine the cause of the trouble condition.  This activity may involve cooperative testing and should be handled as an impaired circuit trouble report.

The BPWG has reached consensus on following the overall Service Assurance process as per the contribution in appendix 12.3

## 8.2	TROUBLE REPORT INFORMATION

The following information should be exchanged when referring the trouble:

- Exchange Carrier Circuit ID (ECCKT).

- Trouble report number or equivalent

- Contact telephone number

- Contact ID (e.g.: name or initials)

- Date and time of reported trouble

- Connecting link ID

- End User telephone number, as appropriate

- Trouble reported

- Other information that may be of assistance (e.g.:  history, subsequent reports)

- Testing information (if requested)

- Access to End User (name, phone number, time of day, etc.)

Each CLEC will provide a trouble reporting number, to handle end users trouble calls.  That number is to be readily available 24 hours a day, 7 days a week.

## 8.3	TROUBLE CLEARANCE REPORTING

When the trouble has been cleared by either the ILEC or the CLEC, the trouble report will be closed out with the originating company and the following information will be exchanged:

- Exchange Carrier Circuit ID (ECCKT).

- Trouble report number or equivalent

- Date and time cleared

- Contact name or initials and telephone number of the persons closing out the report

- Trouble status (temporary or permanent repair)

- Type and nature of trouble found and action taken

- Testing information (if requested)

# 9.	EXCEPTIONS

The following information is provided in an effort to assist CLEC’s and ILEC’s in the resolution of trouble reports that fall outside the normal ticket resolution flow once the original ticket has been closed out. (e.g.: the trouble reoccurs)

## 9.1	REQUEST FOR COOPERATIVE TESTING

When a request for cooperative testing is made, the ILEC or CLEC shall provide the necessary assistance to facilitate the request.  A report will be created for administration of cooperative testing referrals.  Subsequent requests will result in an additional report being created.  In the event that additional trouble reports are created, all relevant information from the prior report/cooperative testing tickets should be cross referenced.

# 10.	ADDITIONAL BILLING

Existing tariffs describe additional billing under certain circumstances. Examples include:

- In the event a trouble arises which the CLEC determines is located within the ILEC’s equipment facility or services, and which the CLEC and the ILEC upon investigation determine is not located in the ILEC’s equipment, facility or services, the ILEC will charge the CLEC for cost incurred.

- Additional acceptance test requested by the CLEC.

Accurate records regarding the work performed for additional billing purposes must be retained.

# 11.	ESCALATION

Escalation is a means of bringing problems to the attention of individuals who have the responsibility and authority to expedite corrective action.

When either the CLEC or the ILEC experiences installation or maintenance difficulties and progress toward resolution is not satisfactory, either company may contact the other company for escalation to a higher level of management.

The rate at which a problem is escalated through successive levels of management should allow each level a reasonable period of time to resolve the problem, before it is presented to the next level for action.

Sample escalation templates for contacts and intervals are provided in Appendices 12.1 and 12.2 for bi-lateral discussions.

# 12.	APPENDICES:

## APPENDIX 12.1: 	Escalation contacts

Trouble Report Centre (TRC) or equivalent, contact and escalation list:

| COMPANY | NAME | TITLE | TELEPHONE NO. |
| --- | --- | --- | --- |
| Carrier (NAME) |  | Trouble Report Centre (TRC) Level I Level II Level III |  |

Installation Report Centre (IRC) or equivalent, e.g. Carrier Services Group, contact and escalation list:

| COMPANY | NAME | TITLE | TELEPHONE NO. |
| --- | --- | --- | --- |
| Carrier (NAME) |  | Installation Report Centre (IRC) Level I Level II Level III |  |

## APPENDIX 12.2 : 		Escalation intervals

| Activity | Level I | Level II | Level III |
| --- | --- | --- | --- |
| Repair Loop Types A & B |  |  |  |
| Repair Loop Type C |  |  |  |
| Installation |  |  |  |

Service Assurance Process Description

| Flow | Description: Service Assurance Process |
| --- | --- |
| 1 | End Customer initiates trouble call. |
| 2 | Service Provider (SP) receives trouble call. |
| 3 | Service Provider validates reported telephone number. If YES: prepare to test trouble - go to Box 5. If NO: go to Box 4. (Box 4 assumes the reported telephone number is not a SP working telephone number (WTN). |
| 4 | Customer is advised to contact the appropriate Service Provider. |
| 5 | Test own network. |
| 6 | Is trouble in your own network ? If YES: go to Box 7. If NO: go to Box 8. |
| 7 | Initiate own repair processes. This includes testing / sectionalizing and repairing the problem in your network / facility / equipment or service. Then go to box 23. |
| 8 | Determine the other (appropriate) Service Provider that the end customer is experiencing problems connecting to or receiving calls from. (Cannot reach or cannot be called by). Where test results indicate trouble with a leased unbundled loop, determine Loop Provider and the circuit number (ECCKT) of the leased loop. If the trouble is related to a trunk outage/failure/malfunction sectionalized to another SP determine the correct exchange company circuit identifier (ECCKT) for that trunk. Then go to box 9. |
| 9 | Document the appropriate trouble ticket report data elements required for trouble referrals between Service Providers. Examples of trouble ticket report types are Unbundled Loops, LNP, Local Interconnection Trunks, Transit Trunks, etc. |
| 10 | Refer the trouble to the other SP or FBP (facilities based provider). |
| 11 | Other Service Provider receives trouble referral. |
| 12 | Other Service Provider validates reported telephone number or circuit number (ECCKT) based on trouble report details and data elements. If YES: prepare to test trouble - go to Box 15. If NO: go to Box 13. (Box 13 assumes the reported telephone number is not a SP WTN or the ECCKT is invalid.) |
| 13 | Refer trouble back to originating Service Provider. |
| 14 | Receive reply from other SP. Go to box 8. |
| 15 | Test own network. |
| 16 | Is trouble in own network ? If YES: go to box 17. If NO: go to box 19. |
| 17 | Initiate own repair processes. |
| 18 | Is originating Service Provider trouble resolved? If YES: Inform originating Service Provider of trouble resolution – go to Box 19. If NO: Go to Box 15. |
| 19 | Advice originating Service Provider of trouble closure / resolution details. |
| 20 | Receive trouble closure / resolution details from other Service Provider. |
| 21 | Is repair notification “No Trouble Found” or “Test Okay”? If YES: go to Box 5. If NO: go to Box 22. |
| 22 | Is customer trouble resolved ? (test to verify this). If YES: Inform End Customer of trouble resolution – go to Box 23. If NO: Refer trouble back to other Service Provider - go to Box 8. |
| 23 | Provide trouble repair notification to end customer - go to box 24 |
| 24 | Receive trouble clearance / resolution detail from Service Provider. |
| 25 | Is trouble resolved? If YES: End If NO: go to Box 5. |

## APPENDIX 12.4: ACRONYMS:

CLEC		Competitive Local Exchange Carrier

COLT		Central Office Line Termination

CSG		Carrier Service Group

CNI	            Customer Network Interface

ILEC                 Incumbent Local Exchange Carrier

LEC		Local Exchange Carrier

LSR		Local Service Request

MDF		Main Distributing Frame

POT		Point of Termination

# Text boxes

Main

Distributing

Frame

Demarcation

Point

Inside Wire

Copper Pairs or

Transmission Systems

Customer Network Interface

Central Office

Loop Termination

Unbundled Local Loop Type A

Demarcation

Point

Main

Distributing

Frame

Inside Wire

Copper Pairs or

Transmission Systems

Customer Network Interface

Central Office

Loop Termination

Unbundled Local Loop Type B

Demarcation

Point

DSX

Inside Wire

Transmission System

Customer Network Interface

Central Office

Loop Termination

Unbundled Local Loop Type C

MDF

Co-location

Area

IDF/MDF

Loop

Type

A or B

Loop Connecting Link

DSX

Co-location

Area

Loop

Type

C

DS 1 Link

No

Yes

Yes

Yes

No

No

CLEC available

for cooperative

test?

Defective

connecting

link?

Trouble proves

in from COLT?

No

Yes

TRC proceeds

with COLT

change as per

CLEC request

CLEC contacts

TRC with new

assignment at a

later time

TRC suspends

the trouble

report

Can CLEC provide new

COLT assignment to TRC

within reasonable

time frame?

Connecting link

change required

TRC closes

trouble report

Connecting Link Repair Process Map

Advises CLEC

and CSG of

work

complete

TRC updates report.

Remarks: proves to

defective connecting

link.  CLEC tariff

charges apply.

TRC updates report.

Remarks: proves to

CLEC equipment.

ILEC tariff charges

apply.  TRC closes

trouble report.

TRC updates

report

Remarks: CLEC

unable to co-op

test

ILEC follows

existing

procedures

trouble

sectionalizes

TRC tests and

TRC receives

trouble report

from CLEC